## Slide 1: Basic i/o
CSE 315 January 2022
Md. Tareq Mahmood
Department of CSE, BUET
8086 Assembly

## Slide 2: 8086 Microprocessor

## Slide 3: General Purpose Registers
8 general purpose registers
  AX - the accumulator register (divided into AH / AL).
  BX - the base address register (divided into BH / BL).
  CX - the count register (divided into CH / CL).
  DX - the data register (divided into DH / DL).
  SI - source index register.
  DI - destination index register.
  BP - base pointer.
  SP - stack pointer.

## Slide 4: Segment Registers
4 segment registers
  CS - points at the segment containing the current program.
  DS - generally points at segment where variables are defined.
  ES - extra segment register, it's up to a coder to define its usage.
  SS - points at the segment containing the stack.

## Slide 5: Special Purpose Registers
IP - the instruction pointer.
Flags Register - determines the current state of the processor.

## Slide 6: Sample Code

## Slide 7: MOV Instruction
Copies the second operand (source) to the first operand (destination).
These types of operands are supported:
  MOV REG, memory
  MOV memory, REG
  MOV REG, REG
  MOV memory, immediate
  MOV REG, immediate
REG:
AX, BX, CX, DX etc.
memory:
variable, etc...
immediate:
5, 3Fh, 10001101b, etc...

## Slide 8: Variable Declaration

## Slide 9: Initialize Data Segment Address
Variables will not have correct value without this

## Slide 10
Code window
Run window
Current Instruction
Variable Inspector

## Slide 11: Single Byte Input
With AH = 1
INT 21H triggers input from console
Stores ASCII value in AL

## Slide 12: Single Byte Output
With AH = 2
INT 21H triggers output to console
Shows character with ASCII value in DL

## Slide 13: What is INT 21H?
DOS can be thought of as a library used to provide a files/directories abstraction for the PC
int 21h is a simple hardware "trick" that makes it easy to call code from this library without knowing in advance where it will be located in memory.
By providing different values to the AH register, different DOS functions can be executed such as opening a file (AH=0x3D) or printing to the screen (AH=0x09).
No need to fully understand now.
Come back later.

## Slide 14: Basic Arithmetic
ADD
SUB

## Slide 15: Print String
Load effective address (LEA) instruction
When AX = 09H
INT 21H triggers character printing from the address in DX
Continue to print until ‘$’ appears