## Slide 1: Assembly Language: Arithmetic and logic instructions
CSE 315
Microprocessors, Microcontrollers, and Embedded Systems

## Slide 2: AND, OR AND XOR
Syntax
  AND destination, source
  OR destination, source
  XOR destination, source
The restrictions of destination and source are the same as ADD or SUB instructions

## Slide 3: AND, OR AND XOR
Effect on flags
SF, ZF, PF reflect the result
AF is undefined
CF, OF = 0

## Slide 4: AND, OR AND XOR
Example
XOR AX, AX
OR AL, 81h
AND AL, 7Fh
Clearing a Register
Set the MSB and LSB while preserving other bits
Clear the Sign Bit

## Slide 5: NOT Instruction
Works on a single operand
Performs one’s complement operation on the destination
Syntax
  NOT destination

## Slide 6: TEST Instruction
Performs similarly to the AND instruction
Except doesn’t write the output on the destination.
Only sets or resets the flags
Syntax
  TEST destination, source
Usually used for flow control

## Slide 7: TEST Instruction
Example
TEST AL,1
Testing a number is even or not

## Slide 8: Shift / Rotate Instructions
Has two possible formats:
  Opcode destination, 1
  Opcode destination, CL
Effect on flags
SF, ZF, PF reflect the result
AF is undefined
CF value changes according to Shift / Rotate Type
OF =1 if result changes sign on last Shift / Rotation

## Slide 9: SHL and SAL instructions
Shifts the bits in the destination to the left
The MSB is shifted into CF
A 0 is shifted to LSB
SAL and SHL generate the same machine code
SHL and SAL

## Slide 10: SHL and SAL instructions
Example
If DH=8AH, CL=3
What is the result of
SHL DH, CL
If DX=8AH, CX=3
What is the result of
SHL DX, CX
DH=50H
CF=0
OF=0
DX=450H
CF=0
OF=0

## Slide 11: Multiplication Using SHL and SAL instructions
A Left shift on a binary number multiplies it by 2
Example
If DH=2H, CL=1
What is the result of
SHL DH, CL
DH=4H
CF=0
OF=0

## Slide 12: Overflow Flag Untrustworthy During Multiplication using SHL or SAL
Example
If DH=80H, CL=2
What is the result of
SHL DH, CL
DH=00H
CF=0
OF=0
CF and OF are not reliable for multiple shifts because multiple shifts are just a series of single shifts and CF, OF only reflect the result of the last shift.

## Slide 13: SHR and SAR instructions
Shifts the bits in the destination to the right
The LSB is shifted into CF
In case of SAR MSB retains its original value
SHR
SAR

## Slide 14: SHR and SAR instructions
SHR should be used for unsigned interpretation as it does not preserve sign
SAR should be used for signed interpretation as it preserves sign

## Slide 15: SHR and SAR instructions
Example
If AL=-15, CL=1
What is the result of
SHR AL, CL
If AL=-15, CL=1
What is the result of
SAR AL, CL
AL=120H
CF=1
OF=1
AL=-8
CF=1
OF=1

## Slide 16: ROL and ROR
ROL and ROR shifts bits in destination to the left and right respectively
For ROL MSB is shifted into the rightmost bit and CF
FOR ROR rightmost bit is shifted into MSB and CF
ROL
ROR

## Slide 17: RCL and RCR instructions
Works similarly to ROL and ROR respectively
For RCL, CF is shifted to LSB and MSB is shifted to CF
FOR RCR, CF is shifted to MSB and LSB shifted to CF
RCL
RCR

## Slide 18: Multiplication instructions
imul source
- Signed multiplication
  mul source
    - Unsigned multiplication
Byte and Word Multiplication (A X B)
  If two bytes are multiplied, the result is a 16-bit word
    A: source
    B: al
    product: ax
  If two words are multiplied, the result is a 32-bit doubleword
    A: source
    B: ax
    Product (ms 16 bits): dx
    Product (ls 16 bits): ax

## Slide 19: Multiplication instructions
source can be a register or memory location (not a constant)
Byte form
  AX=AL*source
Word form
  DX:AX=AX*source
If ax contains 0001h and bx contains FFFFh
  mul bx; dx = 0000h ax = FFFFh
  imul bx ; dx = FFFFh ax = FFFFh (-1)

## Slide 20: Signed Multiplication
C
Assembly
Lable1:
  short int x=0x8000;
  short int y=0xFFFF;
  x=x*y
Label1:
MOV x, 8000H
MOV y, FFFFH
MOV AX, x
MOV BX, y
IMUL BX

## Slide 21: Unsigned Multiplication
C
Assembly
Lable1:
  unsinged short int x=0x8000;
  unsigned short int y=0xFFFF;
  x=x*y
Label1:
MOV x, 8000H
MOV y, FFFFH
MOV AX, x
MOV BX, y
MUL BX

## Slide 22: Multiplication instructions
Effect on flags
SF, ZF, AF, and PF Undefined
CF/OF
  MUL
    0: if upper half result 0
    1: Otherwise
  IMUL
    0: if upper half is sign extension of lower half.
    1: Otherwise

## Slide 23: More Examples
Instruction | Hex Product | DX | AX | CF/OF
MUL BX | FFFE0001 (4294836225) | FFFE (!zero) | 0001 | 1
IMUL BX | 1 | 0000 | 0001 | 0
AX=FFFFh,BX=FFFFh
AX=80h,BX=FFh
Instruction | Hex Product | AH | AL | CF/OF
MUL BX | 7F80 (128) | 7F(!zero) | 80 | 1
IMUL BX | 0080 | 00 (no sign extension) | 80 | 1

## Slide 24: Division instructions
cbw
  convert byte to word
cwd
  convert word to doubleword
div source
  unsigned division
idiv source
  signed division

## Slide 25: Byte and Word Division (A/B)
When division is performed
  two results: the quotient and the remainder
  Quotient and remainder are same size as the divisor
For the byte form,
  Divisor: source; Dividend: ax
  Quotient: al; Remainder: ah
For the word form,
  Divisor: source; Dividend: dx:ax
  Quotient: ax; Remainder: dx

## Slide 26: An Example
;If dx = 0000h, ax = 0005h, and bx = FFFEh (-2)
div bx; ax = 0000h dx = 0005h
idiv bx; ax = FFFEh dx = 0001h

## Slide 27: Division instructions
Effect on flags
Undefined

## Slide 28: Divide Overflow
It is possible that the quotient will be too big to fit in the specified destination (al or ax)
if the divisor is much smaller than the dividend
the program terminates and the system displays the message "Divide Overflow"

## Slide 29: More Examples
Instruction | DX | AX | CF/OF
DIV BX | Divide Overflow |  | 
IDIV BX | FFFE (-2) | FFFF (-1) | Undefined
DX=FFFFh, AX=FFFBh, BX=0002h,
DX:AX=-5 (Signed), DX:AX=4294967291 (Unsigned)
AX=00FBh, BL=FFh
Instruction | AH | AL | CF/OF
DIV BL | FB | 00 | Undefined
IDIV BL | Divide Overflow |  | 

## Slide 30: Sign Extension of the Dividend
Word division
  The dividend is in dx:ax even if the actual dividend will fit in ax
  For div, dx should be cleared
  For idiv, dx should be made the sign extension of ax using cwd
e.g. -1250/7
MOV AX,-1250
CWD ; sign extend
MOV BX,7
IDIV BX

## Slide 31: Sign Extension of the Dividend
Byte division
  The dividend is in ax even if the actual dividend will fit in al
  For div, ah should be cleared
  For idiv, ah should be made the sign extension of al using cbw

## Slide 32: References
Ch 7, 9 Assembly Language Programming – by Yu and Marut