## Slide 1: Microprocessors, Microcontrollers, and Embedded Systems

## Slide 2: BASIC I/O in ATmega32/16

## Slide 3: Ports for I/O
4 different ports for I/O
  A, B, C, D
  8 bit <-> 8 data pins
  Every pin is bidirectional, can be used as input or output

## Slide 6: I/O Ports of ATmega32 (AVR)

## Slide 7: Port Operation Registers
DDRx – Data Direction Register
PORTx – Pin Output Register
PINx – Pin Input Register

## Slide 8: Configuration
  For configuration we have to use the Data Direction Registers
    One register for each port
    DDRx (DDRA, DDRB, DDRC, DDRD)
    Configures each pin as input or output
Pin configuration
  Input – 0
  Output – 1

## Slide 9: C Code Example
DDRA = 0b11111111;
  Sets each bit of port A as output
DDRB = 0b00000000;
  Sets each bit of port B as input
DDRC = 0b01010101;
  ???

## Slide 10: Input
You have to read the PINx register
unsigned char ch; ch = PINA;
What to do if only some of the pins are configured as input ??

## Slide 11: Output
You have to use the PORTx register
PORTB = 0b11111111;
What to do if only some of the pins are configured as output ??

## Slide 12: Write a simple program to set the port B to 0xFF

## Slide 13: C Code
#include <avr/io.h>
int main(void)
{
DDRD = 0b11111111; //initializing portD in //output mode
PORTD = 0b11111111;//writing value to portD
while(1)
{
//TODO:: Nothing
}
}

## Slide 14: What will this code do ??
#include <avr/io.h>
int main(void)
{
DDRD = 0b01111111;
PORTD = 0b11111111;
while(1)
{
//TODO:: Nothing
}
}

## Slide 15: Write a simple program to blink a LED on port B pin 0

## Slide 16: C Code
#include <avr/io.h>
int main(void)
{
unsigned char c = 1;
DDRB= 0b00000001;
while(1)
{
    PORTB = c;
    if(c) c = 0;
    else c = 1;
    delay();
  }
}
void delay()
{
    unsigned char i,j,k;
    for(i=0;i<255;i++)
    for(j=0;j<255;j++)
    for(k=0;k<100;k++);
}

## Slide 17: Write a simple program to animate 8 LEDs connected to PORT B
One LED at a time is ON
The rest are off
At first LED 0 is on, then LED 1, and so on.

## Slide 18: C Code
int main(void)
{
unsigned char c = 0x01;
DDRB= 0xFF;
while(1)
{
PORTB = c ;
if(c==1<<7)c = 1;
else c = c << 1;
delay();
}
}

## Slide 19: Accurately Generating Delay
#include <avr/io.h>
#define F_CPU 1000000 // Clock Frequency
#include <util/delay.h>
int main(void)
{
while(1)
{
//1000 ms delay
_delay_ms(1000);
}
}

## Slide 20: Simple Input
A 8 bit input is connected to PORT A
Show the input state on PORT B

## Slide 21: C Code
int main(void)
{
unsigned char c;
DDRA = 0x00;
DDRB = 0xFF;
while(1)
{
c = PINA;
PORTB = c ;
}
}

## Slide 22: Simple Counter
PA0 is connected with push button
  1 when pressed
PORT B connected to 8 LEDs
Increment count when pressed the push button

## Slide 23: C Code
int main(void)
{
unsigned char c=0,in=0;
DDRA = 0xFE;
DDRB = 0xFF;
PORTB = c;
while(1)
{
in = PINA;
if(in & 0x01)
{
c++;
PORTB = c; }
}
}

## Slide 24: Switch Bouncing
Non-ideal behavior of any switch which generates multiple transitions of a single input.
Causes problems while we are dealing with the logic or digital circuits.

## Slide 25: Switch Bouncing

## Slide 26: C Code - Debouncing
int main(void)
{
unsigned char c=0,in=0;
DDRA = 0xFE;
DDRB = 0xFF;
PORTB = c;
while(1)
{
in = PINA;
if(in & 0x01)
{
c++;
PORTB = c; _delay_ms(1000);
}
}
}

## Slide 27: Write a program to read a byte from PORT A and write it to PORT B
Exercise

## Slide 28: If input (taken from PORTC) is less than 100, send it to PORTB, otherwise, send it to PORTD
Exercise

## Slide 29: Write a program to read a byte from PORT A and write its upper nibble to PORT B (lower nibble) and lower nibble to PORT C (upper nibble)
Exercise

## Slide 30: Discussions on push buttons
This might seem like the reasonable connection
What is wrong with it?

## Slide 31: Discussions on push buttons
When switch is disconnected, input state can be HIGH or LOW
This phenomena is referred to as floating

## Slide 32: Handle Floating

## Slide 33: Pull-Up Resistor

## Slide 34: A deeper look

## Slide 35: A deeper look
When the button is not pressed, the input pin is pulled high. The value of the pull-up resistor controls the voltage on the input pin.
R1 must be smaller enough than R2 to drop less voltage across R1

## Slide 36: A deeper look
When the button is pressed, the input pin is pulled low. The value of resistor R1 controls how much current we want to flow from VCC, through the button, and then to ground.
Large R1 causes more power consumption

## Slide 37: A deeper look
Because of the two opposing factors the resistor value cannot be too high not too less
R1 can be about 1/10th of R2

## Slide 38: Pull Down Resistor

## Slide 39: Enable Internal Pull-Up
If PORTxn is written logic one when the pin is configured as an input pin, the pull-up resistor is activated.
Here, x = A,B,C, or D
n is bit number, e.g., 0,1,2,..., or 7

## Slide 40: Enable Internal Pull-Up
DDRA = 0b11110000;
PORTA = 0b11111111;

## Slide 41: General Discussion
If some pins are unused, it is recommended to ensure that these pins have a defined level.
The simplest method to ensure a defined level of an unused pin, is to enable the internal pullup.

## Slide 42: Readable Code
Use defined constants instead of immediates if possible
They are defined in header files (e.g. io.h)
PORTA = PORTA | (1 << 3)
PORTA = PORTA | (1 << PORT3)
https://github.com/hexagon5un/AVR-Programming/blob/master/AVR-Programming-Library/portpins.h

## Slide 43: Resources
DataSheet
Pull-Up and Pull-Down Resistors
  http://www.resistorguide.com/pull-up-resistor_pull-down-resistor/
More on Pull-Up and Pull-Down resistors
  https://learn.sparkfun.com/tutorials/pull-up-resistors

## Slide 44
☺