## Slide 1: TIMER in atmega32
CSE 315
Courtesy: Muhammad Ali Nayeem, Azad Abdus Salam, Md. Iftekharul Islam Sakib

## Slide 2: Learning Objective
What is timer?
When, how to use timer?

## Slide 3: Time is “money”
An embedded system has to preform various time-related tasks
  Recording the time when an event occurs
  Calculating the time difference between two events
  Performing tasks at specific or periodic time instants
  Creating accurate time delays
  Generating waveforms of certain shape, period or duty cycle

## Slide 4: Software technique?
Can we use CPU to do these tasks?
  Yes!
  But…
    CPU will be busy
    Timing will not be accurate
Need something special?
    Hardware technique

## Slide 5: PROBLEM DELAY_MS
If an ISR is fired during the execution of a delay_ms(),
ISR will be serviced first, then delay will continue
Resulting in more delay than specified
For example,
If you call _delay_ms(1) and some ISR occurs that take 200us to be serviced, _delay_ms(1) takes 1.2ms

## Slide 6: Overview
ATmega32 has 3 timers
  Timer 0, 1, 2
  Timer 1 has the most functionalities
Each timer is associated with
  A counter
  A clock signal
    Internal
    External

## Slide 7: Overview
When the internal system clock is used, a prescaler can be used to make the timer count at a slower rate
Example:
  Suppose the system clock rate = 1Mhz (1μs per cycle).
  Suppose a timer prescaler of 64 is used.
  Then, timer will increment every 64μs.

## Slide 9: PWM
Pulse Width Modulation
A technique for getting analog results with digital means.
An example of PWM in an idealized inductor driven by a ■ voltage source modulated as a series of pulses, resulting in a ■ sine-like current in the inductor.

## Slide 10: Timer 1

## Slide 11: Timer 1
16 bit counter
  prescaler: 8, 64, 256, 1024
Can trigger a timer overflow interrupt
  and other things.. We will learn those in the subsequent lectures
Can trigger an input capture interrupt when an event occurs on the input capture pin
  timer value is stored automatically in a register.
  input capture pin for Timer 1 is ICP1 (D.6)

## Slide 12: Timer 1 – Relevant pins

## Slide 13: Related Registers – Timer1
TIMER/COUNTER1
  TCNT1
  16 bit register that stores the current value of the counter
Timer/Counter 1 Control Registers
  TCCR1A and TCCR1B
  To configure the operations of Timer 1.
Interrupt registers
  TIMSK to enable timer interrupts
  TIFR to monitor status of timer interrupts

## Slide 14: Related Registers – Timer1
4. Input Capture Register
- ICR1
- to store timer value when an event occurs on input capture pin
5. Output Compare Registers

## Slide 15: Timer related interrupts

## Slide 16: Today’s mission
Creating an accurate delay using timer overflow interrupt
Measuring elapsed time between two events

## Slide 17: Let’s start!!!

## Slide 18: MODES

## Slide 19: Timer/Counter 1 Control Register A (TCCR1A)

## Slide 20: Timer/Counter 1 Control Register B (TCCR1B)

## Slide 21: Clock select

## Slide 22: Normal mode

## Slide 23: Timer/Counter Interrupt Mask Register (TIMSK)

## Slide 24: Timer/Counter Interrupt Flag Register (TIFR)

## Slide 25: Write a C code to toggle PORTB every 2 seconds using TIMER 1 Overflow Interrupt

## Slide 26: Creating an accurate delay of 2s
System Default Frequency: 1Mhz
Period: 1µs
With no prescaler TIMER 1 will increment every 1µs
TCNT1 is 16 bit
Timer will overflow every 216 μs.
How many times TIMER1 will overflow ??
In 2S, total TIMER1 overflow

## Slide 27
#include <avr/io.h>
#include <avr/interrupt.h>
volatile int overflowCount;
ISR(TIMER1_OVF_vect)
{
  overflowCount++;
  if(overflowCount==31)
  {
  PORTB = ~PORTB;
  overflowCount = 0;
  }
}
int main(void)
{
  overflowCount = 0;
  DDRB = 0xFF;
  PORTB = 0xFF;
  //configure timer
  TCCR1A = 0b00000000; // normal mode
  TCCR1B = 0b00000001; // no prescaler, internal clock
  TIMSK = 0b00000100; //Enable Overflow Interrupt
  sei(); //Global Interrupt Enable
  while(1);
}

## Slide 28: Appendix
Why volatile variable?
  http://www.avrfreaks.net/forum/whats-volatile-variable

## Slide 29: Measure the time for a demo C Code to execute

## Slide 30: Measuring elapsed time
When no prescalling

## Slide 31: Measuring elapsed time
16 Bits
Counts to overflow
Find times between increments (Period)
For no prescaler, frequency, F = / 1 =
Period, P = 1 / F = =
Number of overflows = n
Total count, C = TCNT1
Total time =

## Slide 32
// In micro seconds

## Slide 33: Measure the period of a square wave

## Slide 34: Measure period
When a capture is triggered, the 16-bit value of the counter (TCNT1) is written to the Input Capture Register (ICR1).

## Slide 35: Measure period
TCCR1B = 0b11000001;
Say, period of input signal is less than .

## Slide 36
volatile uint16_t period;

## Slide 37: Measure the period of a square wave
Exercise:
No assumption on frequency
Period of input signal is greater than .
Need to consider overflow count.
Left as an execise to the reader.